## Slide 1: GHS and Agriculture Part 2 – The GHS and how it applies to pesticides and fertilizers
Notes: 3 round logos : FAO

## Slide 2: GHS and agriculture Part 2 – The GHS and how it applies to pesticides and fertilizers
This second part of the presentation on “GHS and agriculture” complements Part 1 (available separately). Part 1 reviews:
  the importance and relevance of the GHS for the agricultural sector, at the national, regional and international levels
  the benefits of implementing the GHS in agriculture
  the process for implementing the GHS at the country level

## Slide 3: GHS and agriculture Part 2 – The GHS and how it applies to pesticides and fertilizers
A. GHS and pesticides
B. GHS and fertilizers
C. References
Overview
Notes: In this Part 2 of the presentation on “GHS and agriculture”, you will learn:
More about how and why the GHS is relevant for pesticides and fertilizers, with a particular focus on pesticides.
Further technical aspects of GHS implementation in agriculture and how – in practice -- to apply the classification criteria and prepare pesticide labels.
Who is this presentation for?
Primarily for policy makers in the agriculture sector.
But also for anyone who would like to understand more about the relevance of GHS for the agricultural sector.
More specifically for this Part 2: people who would like to know more about the technical aspects of GHS implementation in agriculture, how – in practice -- to apply the classification criteria and prepare labels & SDS, please refer to introductory information in sections A5, and C. And refer to the FAO Pesticide Registration Toolkit at: https://www.fao.org/pesticide-registration-toolkit/special-topics/globally-harmonized-system-of-classification-and-labelling-of-chemicals-ghs/introduction-to-the-ghs/en/

## Slide 4: A. GHS and pesticides
Elements of GHS and their relevance to pesticides
Do all hazards relate to pesticides? Do all GHS elements apply to agriculture (building block approach)?
GHS is the recommended hazard classification system for pesticides - But my country is using the WHO classification … how is it related and how is it different to the GHS?
My country has used the WHO classification and is applying the FAO color coding /color bands. What does it mean if my country now implements the GHS?
GHS and pesticides a) classification and b) labelling - How to proceed in practice?

## Slide 5: A1. Elements of GHS and their relevance to pesticides

## Slide 6
The GHS contains:
harmonized criteria for classifying substances and mixtures according to their physical, health and environmental hazards; and
harmonized hazard communication elements, including requirements for labelling and safety data sheets (SDS), to make users aware of the hazards of the chemicals they are exposed to.
GHS vocabulary for pesticides
Substances: active ingredients (“a.i.”)
Mixtures: pesticide products or pesticide formulations
Main elements of the GHS
Notes: The GHS contains internationally harmonized criteria for classification of chemical substances and mixtures by type and severity considering physical, health and environmental hazards.
The GHS also proposes harmonized communication elements, such as labels and safety data sheets, to make users aware of the hazards of the chemicals they are exposed to.
The GHS thus aims to enhance the protection of human health and the environment during the handling, transport, and use of chemicals.

## Slide 7
Criteria for classification
Safety Data Sheets
Labels
Is it hazardous?
How hazardous is it?
How do you make
people aware of the hazards?
Physical
Health
Environment
Hazard communication
Hazard assessment
Main elements of the GHS
Notes: SDSs are primarily for use by workers (for example, handlers, warehouse workers, agricultural workers, pre- and post-application workers, and vendors) in workplaces involved in pest control product application and handling.
SDSs are also commonly used by emergency responders (including health professionals), consumers, and those involved in the transportation of dangerous goods.

## Slide 8
Criteria for classification
Is it hazardous?
For what hazards
Physical
Health
Environment
Hazard assessment
Hazard Class (and sub-classes)
Hazard Category (generally 1-5)
How hazardous is it?
Low
High
1 | 2 | 3 | 4 | 5
Main elements of the GHS
Notes: Sub-classes for different exposure routes (e.g. oral, dermal, inhalation)
Chemicals with the most severe effect within a hazard class are generally placed in Category 1 and then the number increases with decreasing severity. Some physical hazard classes are differentiated according to severity using an alternative to the numbering system.

## Slide 9: GHS Signal words (2)
Labels
How do you make
people aware of the hazards?
Hazard communication
Danger - severe hazard
Warning – less severe hazard
GHS Hazard Statements
GHS Pictograms (9)
Communication elements
e.g. Fatal if swallowed toxic if inhaled
Precautionary statements and pictograms
(not part of the GHS)
Safety Data Sheets
(16 sections)
Main elements of the GHS
Notes: Notes:
pictogram = symbol and other graphical elements
More on the 16 sections of a SDS in the general presentation on GHS (available separately).
Precautionary pictograms are not strictly part of the GHS, but information is provided in the GHS text with examples of precautionary pictograms, which can be used where allowed by the competent authority.

## Slide 10
Hazard pictograms
Signal words
Hazard statements
Precautionary statements
Precautionary pictograms
Additional information on a pesticide label
Hazard colour band – see section A.4
Product identity and content
Supplier identifier
Directions for use, including target pests and crops, and disposal
Supplemental information: tactile warning, product or user category, first aid and medical advice, accidental spills advice, release date of the product, shelf-life or expiry date, legal responsibility/ disclaimer, QR-Code, contact at national or regional poison centre
GHS hazard communication elements
At the discretion of competent authorities (country-, hazard- and use-specific)
Pesticide Labelling
Reference: FAO/WHO labelling guidelines
Notes: A label is defined as an appropriate group of written, printed or graphic information elements concerning a hazardous product, selected as relevant to the target sector(s), that is affixed to, printed on, or attached to the immediate container of a hazardous product, or to the outside packaging of a hazardous product.
The GHS hazard communication elements are
Pictograms
Signal words
Hazard statements
Precautionary statements (examples in Annex 3 of the GHS) and pesticide-specific examples in the FAO guidelines on labelling
As many countries have placed the responsibility on the applicant to submit a proposal for classification and a draft label for the pesticide product as part of the dossier, the registration authority will have to check the label accuracy during dossier evaluation.
Photo: FAO/WHO labelling guidelines

## Slide 11
Note about precautionary statements and pictograms  not part of GHS
not internationally harmonized and rather defined nationally
often defined by risk assessments conducted during pesticide registration to mitigate the identified risks (can be based on hazards too, e.g. eye damage/eye irritation)
The GHS provides suggestions for precautionary statements and associates them with specific hazard classes of pesticides (Annex 3 of GHS).
The FAO/WHO guidance on pesticide labelling provides additional examples of precautionary statements, not listed in the GHS, that may be relevant to specific situations of pesticides.
Pesticide Labelling
Notes: Pictograms: FAO labelling guidelines

## Slide 12: A2. Do all hazards relate to pesticides? Do all GHS elements apply to agriculture?
About the building block approach

## Slide 13
The hazard class describes the type of hazard
GHS includes:
17 Physical hazard classes (GHS Chapters 2.1 – 2.17)
10 Health hazard classes (GHS Chapters 3.1 – 3.10)
2 Environmental hazard classes (GHS Chapters 4.1 – 4.2)
Are they all relevant for pesticides?
GHS Hazard classes
Notes: The hazard class describes the type of hazard. The hazard classes are grouped into physical hazards, health hazards and environmental hazards. The most recent edition of GHS contains 17 physical hazard classes, ten health hazard classes, and two environmental hazard classes. The classification criteria for physical hazards are found in Part 2 of the GHS, while those for health and environmental hazards are found in Parts 3 and 4, respectively.

## Slide 14
Hazard class | (Likely) Relevant for pesticides
Explosives | 
Flammable gases | Yes
Aerosols and chemicals under pressure | Yes
Oxidizing gases | Yes
Gases under pressure | Yes
Flammable liquids | Yes
Flammable solids | 
Self-reactive chemicals | 
Pyrophoric liquids | 
Pyrophoric solids | 
Self-heating chemicals | 
Water reactive – emits flammable gases | Yes
Oxidizing liquids | Yes
Oxidizing solids | Yes
Organic peroxides | Yes
Corrosive to metals | 
Desensitized explosives | 
Not all physical hazards are relevant for pesticides.
X
X
Pesticides and GHS Physical Hazards
Notes: The physical hazard classes consider effects such as
Explosivity
Flammability
Oxidizing potential
Metal corrosion
Chemicals under pressure
Not all physical hazards are relevant for pesticides.
Generally, if a pesticide fulfils the criteria of any of the physical hazards which are not marked as relevant in the table, it will not be authorized for use in the first place (e.g. a pesticide would not be explosive).
Generally, it is not possible to calculate classification of a mixture from the physical hazard classification of the active ingredient(s) which means that testing of the product itself is necessary.
If a pesticide product poses more than one GHS physical hazard, all relevant symbols, signal words and hazard statements should be on the label. (add: about “precedence” in notes).
The criteria for physical hazard classification are aligned with the UN recommendations on the Transport of Dangerous Goods.

## Slide 15
Health hazard classification of products is generally based on the available information for the individual classified ingredients and their concentrations in the product (formulation)
Classification is derived using either a calculation method or by applying cut-off values/concentration limits methods (additive or non-additive).
Hazard class | Mixture classification method
Acute toxity | Calculation
Skin corrosion/irritation | Cut-off value/concentration limit, additive
Serious eye damage/eye irritation | Cut-off value/concentration limit, additive
Respiratory or skin sensitization | Cut-off value/concentration limit, non-additive
Germ cell mutagenicity | Cut-off value/concentration limit, non-additive
Carcinogenicity | Cut-off value/concentration limit, non-additive
Reproductive toxicity | Cut-off value/concentration limit, non-additive
STOT – single exposure | Cut-off value/concentration limit, non-additive
STOT – repeated exposure | Cut-off value/concentration limit, non-additive
Aspiration toxicity | Cut-off value/concentration limit, additive
All health hazards are relevant for pesticides
Pesticides and GHS Health Hazards
Notes: All health hazard classes apply to pesticides
Each class is further differentiated in hazard categories based on the severity of reaction or strength of available evidence, for instance human data versus animal test data.
The health hazard classification of products (mixtures) is generally based on data on the active ingredient(s).
For acute toxicity, a calculation method is applied on numerical indices of acute toxicity (acute toxicity estimate, ATE) for each classified ingredient and their percentage in the product.
For other hazard classes, a cut-off value/concentration limit approach is applied. The approach can be either additive considering the sum of concentration of all ingredients classified for a certain hazard, or non-additive where a single substance above the cut-off value/concentration limit justifies classification.
Adverse effects can be additive and non-additive.
The additive effects are dose-dependent and include: Acute toxicity; Skin corrosion and irritation; Serious eye damage and irritation; and aspiration hazards. In such cases, the principle of additivity applies. Hazard categories are established by using additivity formulas for acute toxicity and the other categories are defined according to the concentration ranges of the sum of the concentration of the classified ingredients in each class.
Non-additive adverse effects are not dose-dependent and include: Respiratory or skin sensitization; mutagenicity; carcinogenicity; toxic to reproduction and Specific Target Organ Toxicity. Additivity formulas do not apply in these cases. The classification criteria indicate only the upper concentration limit of which the mixture is classified when there is at least one ingredient classified in these categories and is present in a concentration above this limit, without applying any formula. A single substance above the cut-off value/concentration limit can justify classification.

## Slide 16
Hazard class | Hazard category |  |  |  |  | 
3.1 Acute toxicity Oral Dermal Inhalation |  |  |  |  |  | 
 | 1 | 2 | 3 |  | 4 | 5
 | 1 | 2 | 3 |  | 4 | 5
 | 1 | 2 | 3 |  | 4 | 5
3.2 Skin corrosion/irritation | Corrosive |  |  |  | Irritant | 
 | 1A | 1B | 1C |  | 2 | 3
3.3 Serious eye damage | Corrosive |  |  |  | Irritant | 
Skin corrosion/irritation | 1 |  |  |  | 2A | 2B
3.4 Sensitization Respiratory Skin |  |  |  |  |  | 
 | 1A |  |  | 1B |  | 
 | 1A |  |  | 1B |  | 
Decrease in severity
GHS 9th revised edition (2021)
Health hazard classes and categories
Notes: Example for some health hazard classes
The health hazard class Acute toxicity has five hazard categories. The hazard class distinguish between route of exposure (oral, dermal and inhalation).
Skin corrosion/irritation and Serious eye damage distinguish between irreversible (corrosion) and reversible (irritation) to the skin or eye.
Sensitization makes a distinction between effects on the respiratory tract (e.g. asthma) and skin (e.g. rashes, nettle fever). Respiratory sensitization classification is based on human evidence.

## Slide 17
Classification |  |  | Labelling |  | 
Hazard class | Hazard category |  | Pictogram | Signal word | Hazard statement
Acute toxicity | 1 | Oral |  | Danger | Fatal if swallowed
 |  | Dermal |  |  | Fatal in contact with skin
 |  | Inhalation |  |  | Fatal if inhaled
 | 2 | Oral |  | Danger | Fatal if swallowed
 |  | Dermal |  |  | Fatal in contact with skin
 |  | Inhalation |  |  | Fatal if inhaled
 | 3 | Oral |  | Danger | Toxic if swallowed
 |  | Dermal |  |  | Toxic in contact with skin
 |  |  |  |  | Toxic if inhaled
 |  | Inhalation |  |  | 
 | 4 | Oral |  | Warning | Harmful if swallowed
 |  | Dermal |  |  | Harmful in contact with skin
 |  |  |  |  | Harmful if inhaled
 |  | Inhalation |  |  | Harmful if inhaled
 | 5 | Oral | No pictogram | Warning | May be harmful if swallowed
 |  | Dermal |  |  | May be harmful in contact with skin
 |  | Inhalation |  |  | May be harmful if inhaled
Higher
Lower
Severity
Acute toxicity (3.1)
Notes: Let’s see further one example for acute toxicity.
This slide is based on entries in the summary tables in Annex 1 of GHS. Here you can see how hazard information related to the five categories in the hazard class Acute toxicity are communicated by pictograms, signal words and hazard statements.
Please note how the information changes when the severity of the effect decreases, The skull and crossbones symbol are used for the top three categories, the exclamation mark for Category 4 while no pictogram is used for Category 5.
You can also note that the hazard statements change from ”fatal” to ”toxic”, ”harmful” and finally ”may be harmful”.

## Slide 18
The persistency (degradation rate) of a pesticide in the environment and its bioaccumulating potential are important to consider in long-term hazard classification.
Chemicals covered by the Montreal protocol
Hazard class | Relevant for pesticides
Acute (short-term) hazard and chronic (long-term) hazard for the aquatic environment | Yes
Hazardous to the ozone layer | Yes (only Methyl Bromide)
All environmental hazards are relevant for pesticides
Pesticides and GHS Environmental Hazards
Notes: The GHS currently contains only two environmental hazards; these are both relevant for pesticides.
For labelling purposes, the pesticide formulation or end-user product, and not the active ingredient, should in principle be classified.
Hazardous to the aquatic environment means the intrinsic property of a substance or mixture to cause harm to an organism upon aquatic exposure. The hazard class covers both acute (short-term) and chronic (long-term) exposure. The duration of long-term exposure is determined by the life-cycle of the test organism. Important factors to consider when classifying chemicals for long-term aquatic toxicity are degradation rate and bioaccumulating potential.
Degradation means the decomposition of organic molecules to smaller molecules and eventually to carbon dioxide, water and salts.
Bioaccumulation means net result of uptake, transformation and elimination of a substance in an organism due to all routes of exposure (i.e. air, water, sediment/soil and food).
Hazardous to the ozone layer covers the controlled substances listed in Annexes to the Montreal Protocol and mixtures containing at least one of these substances as ingredient(s) at a concentration ≥ 0.1%. There is only one pesticide in the Montreal Protocol (Methyl Bromide).

## Slide 19
Generally, yes  pesticides are mostly hazardous products.
But it depends on content and composition (of all ingredients, including adjuvants/co-formulants).
If one ingredient is “classified”, then the pesticide product would need to be “classified”.
Not classified if concentration is lower than certain cut-off values or concentration limits (% depends on hazard classes and categories).
Should all pesticides be “classified”?

## Slide 20
Generic cut-off values or concentration limits e.g. for the health and environmental hazards.
In some cases, with some pesticides, the cut-off values may not be appropriate and lead to an “under-classification” of the formulation (e.g. aquatic hazards).
Should all pesticides be “classified”?
Cut-off values and generic concentration limits for different classes of hazard
Notes: * warning in GHS (cut-off could be lower: 1.3.3.2.2)
Example:
Aquatic Hazards
(Toolkit) When a mixture contains ingredients classified as Acute 1 or Chronic 1, attention should be paid to the fact that such ingredients, when their acute toxicity is well below 1 mg/L and/or chronic toxicity is well below 0.1 mg/L, contribute to the toxicity of the mixture even at a low concentration.
Active ingredients in pesticides often possess such high aquatic toxicity. Under these circumstances the application of the normal cut-off values/concentration limits may lead to an “under-classification” of the mixture. Therefore, multiplying factors should be applied to account for highly toxic ingredients.

## Slide 21
Identity of ingredient substances
Hazard classification of ingredient substances
Concentration of ingredient substances
For formulations, the classification generally requires knowledge on the identity of the ingredients, their individual classification, and their concentration in the pesticide product (formulation).
Classification of the formulation for a specific hazard can be based on testing (mandatory for physical hazards), by summation of the concentration of the classified ingredients or by using cut-off values/concentration limits.
Classification of Pesticide Products - Process
Notes: The classification of mixtures generally requires knowledge of the ingredient substances (i.e. active ingredients and other co-formulants), their concentration, and individual classification.

## Slide 22
Adoption:
  In full with additions as appropriate not to reduce protection of human health and the environment compared with existing systems currently in place
  In parts in order to minimize changes to existing systems
Implementation by choosing the building blocks necessary to construct an appropriate approach by considering the needs of a given sector
Consistency is important: If a competent authority chooses to cover a certain hazard when it adopts the GHS, it should also adopt all of the harmonized elements associated with that hazard.
Adopting GHS the Building Block Approach
Notes: In order to facilitate a smooth transition from an existing classification and labelling system to one that implements GHS, the building block approach for GHS adoption was introduced. The GHS can be adopted in full, with additions as appropriate not to reduce protection of human health and the environment compared with a systems currently in place.
The GHS covers a broad range of chemicals, hazards, and sectors in its scope. In order to accommodate all of the needs of these different groups, the GHS is based on what has been termed the “building block approach”. The concept is that the GHS includes all of the tools needed by all sectors to protect those exposed in their different areas/sectors, but it is also recognised that since the needs of these areas are different, the appropriate coverage will be as well.
Hazard classes are a collection of “building blocks” and within a hazard class, each hazard category can be seen as a building block. Within certain criteria, countries can choose which building blocks to adopt.
Consistency - If a competent authority chooses to cover a certain hazard when it adopts the GHS, it should also adopt all of the harmonized elements associated with that hazard. However, it is not necessary for each competent authority to cover all hazard classes, or hazard categories within a class. Countries can determine which of the building blocks will be applied in different parts of their systems (consumer, workplace, transport, pesticides, etc.). As long as the hazard classes and categories covered by a sector or system are consistent with the GHS criteria and hazard communication requirements, it will be considered appropriate implementation of the GHS.

## Slide 23
Examples:
US some hazard classes that were part of the pre-existing standard have been retained (and not part of GHS)
Australia the Australian Regulations only adopt acute toxicity categories 1 to 4.
EU CLP includes all GHS hazard classes but not all hazard categories, e.g. acute toxicity cat. 5, flammable liquids cat. 4 and skin irritation cat. 3.
Adopting GHS the Building Block Approach
Notes: The US Hazard Communication Standard that implements GHS retains some hazard classes that were part of the pre-existing standard.
Australia
Under the GHS, chemicals can be allocated to one of five toxicity categories for each exposure route (oral, dermal or inhalation), the criteria for these categories are set out in Table 3.1.1 of the GHS. Note that the model Australian (WHS) Regulations only adopt acute toxicity categories 1 to 4.
In the EU, Acute Toxicity Category 5 has not been adopted as a corresponding hazard category was not part of the pre-existing hazard classification system.

## Slide 24: A3. GHS is the recommended hazard classification system for pesticides. “But my country is using the WHO classification … how is it related and how is it different from GHS?”
Notes: Reminder:
The FAO/WHO guidance on pesticide labelling recommends that GHS should be the only classification scheme used for labelling (health) hazards of pesticides.

## Slide 25
In the pesticide sector, countries are very familiar with the WHO Classification of Pesticides
Since its first publication in the 1970s, it has been widely used both to classify pesticides (e.g., for labelling) and as a decision-making tool.
WHO Classes Ia and Ib (“extremely hazardous” and “highly hazardous”) pesticide products have been strictly regulated or are not allowed to be registered in many low- and middle-income countries.
The WHO classification may seem simpler, more accessible and practical than the GHS. It is often used by jurisdictions that do not have sufficient resources to carry out toxicological evaluations of pesticides and have not yet been able to implement the GHS.
The WHO Recommended Classification of Pesticides by Hazard (WHO, 2019)

## Slide 26
Both systems provide methods to classify pesticides by hazard.
From the 2009 revision, the WHO classification system is aligned with the GHS.
However, there are some differences.
The WHO system
classifies substances or active ingredients (a.i) mainly according to their acute oral and dermal toxicity and associated LD50 values (chronic toxicity- CMR - has also been taken into account for some a.i.).
  The rest of the other hazards covered by the GHS, i.e. other health hazards, all physical and environmental hazards, are not covered by the WHO document.
provides tables listing the pesticide a.i. by names (calculations still need to be done for the products i.e. mixtures).
needs to be regularly updated.
does not provide any communication elements, i.e. no pictograms, no colors.
The WHO Recommended Classification of Pesticides by Hazard and its link to the GHS
Notes: In the WHO classification
most pesticides are there, maybe the most recent ones are not included
acute oral and dermal toxicity is provided as LD50 values
lists peer-reviewed data on acute toxicity (internationally acceptable evaluations)
From the 2009 revision, the WHO classification system is aligned with the GHS = it refers to the GHS. The GHS Acute Toxicity Hazard Categories for acute oral or dermal toxicity are presented in the WHO document (column 7 of Tables 1-5 in Part II). The value (i.e. GHS category) shown in the 7th column is the Acute Toxic Hazard Category according to the GHS criteria, which in turn is derived from the acute toxicity estimate value for the substance. In the majority of cases the acute toxicity estimate will be the experimentally-derived LD50 value for oral exposure.
In summary, GHS is a (more) comprehensive and globally recognized system applicable to all (most) chemicals and many hazards, while the WHO classification specifically addresses the hazards (for acute tox and some chronic tox) associated with pesticides.
Note: Also, from the 2009 revision, to more closely align with GHS, the WHO document presents a single scheme instead of separate schemes for liquids and solids.

## Slide 27
Some more differences:
Vocabulary : WHO “class” = GHS “category”
Slight differences in categories
WHO
Ia
Ib
II
III
U (Unlikely to present acute hazard in normal use)
The WHO Recommended Classification of Pesticides by Hazard and its link to the GHS
Notes: WHO classes Ia & Ib are equivalent to GHS categories 1 and 2

## Slide 28
FAO/WHO Guidance on pesticide labelling recommends:
use of the GHS as the only classification scheme for labelling of pesticides, to replace older classification systems such as the WHO classification.
progressive adoption of the GHS for classification and labelling health hazards of pesticides.
To avoid conflicts in classification and confusion for users, during transition to the GHS:
the two classifications should not be mixed.
for instance, the WHO classification for acute toxicity should not be combined with the GHS classification for other health hazards.
Transitioning from WHO Classification to GHS
Notes: Reminder: The FAO/WHO guidance on pesticide labelling recommends that GHS should be the only classification scheme used for labelling health hazards of pesticides.

## Slide 29
Planning the transition
To be done at a fixed date.
To be applied for all pesticide labels at the same time.
Give sufficient advance warning to pesticide manufacturers and importers.
Adapt training and materials on pesticides to inform pesticide users about any changes in hazard symbols, signal words and hazard statements.
Transitioning from WHO Classification to GHS
Notes: Sufficient advance warning should be given to pesticide manufacturers and importers so they can design new labels and prepare the logistics of the transition.
Note: Countries that still apply the WHO 2004 classification and wish to implement the GHS for pesticide labelling should do so directly and not apply the WHO 2009/2019 classification as an intermediate solution, as this would result in two subsequent changes of classification and labelling, leading to increased costs for the pesticide industry and probably greater confusion among pesticide users.
In conclusion, countries should adopt the GHS for their national classification and labelling scheme but can still consult to the WHO document for the lists of pesticides, a practical tool which is anyway aligned to the GHS categories.

## Slide 30: A4. My country has used the WHO classification and is applying the FAO colour coding /colour bands.
What does it mean if my country now implements the GHS?

## Slide 31
Many countries, especially LMICs, require hazard colour “bands” on their pesticide labels.
These color codes are often used quickly to convey information about the nature of the hazard and the potential risks associated with the pesticide use.
Clarification: the colour bands have been developed by FAO (since the 1980s). (They are neither part of the GHS nor the WHO classifications.)
Reference in the GHS
Pesticide colour bands
Notes: The FAO-WHO labelling standard continues to be widely used by countries worldwide, including Africa with 83% from the respondents and S.E. Asia with 75% of the respondents (to a 2018 FAO/WHO survey)
These bands of specific colours are linked to the hazard classification of the product and are printed horizontally at the bottom part of the label.
They have been developed by FAO as part of the Pesticide Labelling Guidance (since the 1980s).
The GHS (nor WHO) does not prescribe specific color coding for pesticide labeling.

## Slide 32
FAO suggests a colour band scheme to indicate acute and severe chronic (CMR) health hazards of pesticide products. Since 2022, it is only based on the GHS categories.
It is strongly recommended that the colour band scheme be the same within a region to prevent countries selling pesticides with different hazard colour bands.
Also, it is recommended that a red colour band be used for the GHS hazard CMR Categories 1 and 2 products, regardless of the acute toxicity color code.
Pesticide colour bands in FAO guidance
Notes: In previous versions of the FAO/WHO guidance on labelling, FAO introduced a colour band scheme to indicate (mainly) acute health hazards of pesticide products, based either on the WHO Classification of pesticides by hazard or on the GHS classification. In the 2021 revised edition, a revised colour band scheme is devised based only on the GHS classification.
It is now (since 2022) recommended that a colour band be used to denote both acute and severe chronic (i.e. carcinogenicity, mutagenicity and reproductive (CMR) toxicity) human health hazard classifications, to facilitate understanding by the pesticide user. The same colour is usually not permitted elsewhere on the label, except “red” which is also used for the hazard symbols under the GHS classification, regardless of the colour band.

## Slide 33
Pesticide colour bands in FAO guidance
Notes: In addition to the GHS label elements, the FAO/WHO Guidance includes colour banding as a means to further communicate the hazard.
Red is used for the most severe hazards, then yellow and finally blue. Grey is used for products not classified. In this slide you see label guidance for products classified for acute toxicity in the left table.
Severe chronic toxicity includes the GHS hazard classes for carcinogenicity, (germ cell), mutagenicity and reproductive toxicity and the label guidance (red) is shown in the right table.

## Slide 34
If or when your country applies the GHS for pesticides, you can continue to use the colour bands.
As recommended by FAO, colour bands should be associated with the precautionary pictograms and not mixed with the GHS hazard pictograms.
Add photo example
Pesticide colour bands
Notes: Here are some examples of some precautionary pictograms, as recommended by FAO/WHO.
However, countries may have developed some national ones.

## Slide 35: A5. GHS and pesticides - classification and - labelling
How to proceed in practice?

## Slide 36
Main references and tools
Notes: 1. GHS Purple Book: https://unece.org/about-ghs and the 10th edition at: https://unece.org/transport/dangerous-goods/ghs-rev10-2023
2. FAO/WHO Guidance on Good Labelling Practices for Pesticides (2022)
https://www.fao.org/publications/card/en/c/e69a681a-1844-4acf-8773-e61f94dfabdb
3. FAO Pesticide Registration Toolkit: https://www.fao.org/pesticide-registration-toolkit/en/
And its pages on the GHS and pesticides: https://www.fao.org/pesticide-registration-toolkit/special-topics/globally-harmonized-system-of-classification-and-labelling-of-chemicals-ghs/introduction-to-the-ghs/en/

## Slide 37
In the FAO Pesticide Registration Toolkit:
A GHS-dedicated section provides practical support and a recommended two-step process for:
  1) hazard classification and
  2) preparation of a label.
Also, 2-3 practical approaches for hazard classification of a pesticide product are recommended, depending on the human resources available at the national registration authority.
Applying the GHS to pesticides… In practice
Notes: FAO Pesticide Registration Toolkit: https://www.fao.org/pesticide-registration-toolkit/en/
And its pages on the GHS and pesticides: https://www.fao.org/pesticide-registration-toolkit/special-topics/globally-harmonized-system-of-classification-and-labelling-of-chemicals-ghs/introduction-to-the-ghs/en/

## Slide 38
Notes: How to find the GHS-dedicated section
Select « Special topics » in the top menu
Choose the GHS tab in the left-hand side menu
Click on the « The classification process in practice »

## Slide 39: B. GHS and fertilizers

## Slide 40
Fertilizers are chemicals, so are also subject to GHS.
Less test data are required for authorization than for pesticides
  This often results in data not normally being available for the fertilizer products
In order to classify fertilizers without the need for testing, alternative procedures proposed by the GHS manual itself should be used. However, for physical hazards, testing of the product itself is necessary.
Add photo example
GHS applies to fertilizers too

## Slide 41
GHS applies to fertilizers too
Not all classes of hazards listed by the GHS are applicable to fertilizers
The main hazard classes that apply are:
Physical hazards
  Oxidizing solids
  Corrosive to metals (applies only to aqueous solutions of fertilizers)
  Explosives
Health hazards
  Acute toxicity
  Skin corrosion/irritation
  Serious eye damage/eye irritation
  Respiratory or skin sensitizers
  Toxic to reproduction (in particular, boron compounds)
  Specific target organ toxicity — single exposure and repeated exposure
Environmental hazards
  Hazardous to the aquatic environment — acute and chronic

## Slide 42
Similar classification and labelling process as for pesticides can be followed:
  look for (reliable and quality) test data for physical, health and environmental hazards.
  in the absence of data, find available hazard data for each ingredient of the fertilizer (from reliable databases and international sources).
  obtain the hazard classification for each ingredient.
  get also SDSs from suppliers.
  check similar fertilizers in terms of content.
  depending on the concentration / composition of the fertilizer, classify the product and prepare the label and SDS.
GHS applies to fertilizers too

## Slide 43
GHS-compliant fertilizer labels
Notes: Some examples of a general nature
Photos: internet

## Slide 44: C. References and tools

## Slide 45: References and tools
General
E-learning course on GHS (UNITAR) – on general chemicals
IOMC (Inter-Organization Programme for the Sound Management of Chemicals) Toolbox – scheme on GHS
FAO Pesticide Registration Toolkit and section on GHS
For inspectors, for regulators involved in pesticide label review, for industry involved in preparing pesticide labels
Existing hazard classifications by national and regional authorities and by international bodies (see FAO Toolkit)
FAO/WHO Guidance on Pesticide Labelling (2022)
Notes: UNITAR E-Learning course: https://cwcourses.unitar.org/
IOMC Toolbox: https://iomctoolbox.org/
FAO Pesticide Registration Toolkit https://www.fao.org/pesticide-registration-toolkit/en/
FAO Pesticide Registration Toolkit - Section on the GHS and pesticides: https://www.fao.org/pesticide-registration-toolkit/special-topics/globally-harmonized-system-of-classification-and-labelling-of-chemicals-ghs/introduction-to-the-ghs/en/
Specific hazard classifications and lists for pesticides https://www.fao.org/pesticide-registration-toolkit/information-sources/hazard-classifications/en/
FAO/WHO Guidance on Good Labelling Practices for Pesticides https://www.fao.org/publications/card/en/c/e69a681a-1844-4acf-8773-e61f94dfabdb

## Slide 46
For more information, please contact UNITAR
https://www.unitar.org/sustainable-development-goals/planet/our-portfolio/globally-harmonized-system-classification-and-labelling-chemicals