## Slide 1: Hazard classification
Notes: In this presentation you will be able to learn how hazards are classified according to the GHS.

## Slide 2
1
2
3
4
  Hazard classes
  Hazard categories
  Classification of substances
  Classification of mixtures
Topics
Notes: The hazards are distinguished by nature or type and further divided according to the severity of the effect or the quality of the data available. The GHS contains classification criteria that can be applied on pure substances as well as on mixtures of substances.

## Slide 3
1
  Hazard classes

## Slide 4
Hazard classes
GHS includes:
17 Physical hazard classes (GHS Chapters 2.1 – 2.17)
10 Health hazard classes (GHS Chapters 3.1 – 3.10)
2 Environmental hazard classes (GHS Chapters 4.1 – 4.2)
The hazard class describes the type of hazard
Notes: The hazard class describes the type of hazard. The hazard classes are grouped into physical hazards, health hazards and environmental hazards. The most recent edition of the GHS contains 17 physical hazard classes, ten health hazard classes, and two environmental hazard classes. The classification criteria for physical hazards are found in Part 2 of the GHS, while those for health and environmental hazards are found in Parts 3 and 4, respectively.

## Slide 5
The physical hazard classes covers properties such as:
The GHS classification criteria for physical hazards are adopted from the UN Manual of Tests and Criteria
Physical hazards
Flammability
Explosivity
Oxidising potential
Metal corrosion
Gas under pressure
2.1 Explosives
2.2 Flammable gases
2.3 Aerosols and chemicals under pressure
2.4 Oxidising gases
2.5 Gases under pressure
2.6 Flammable liquids
2.7 Flammable solids
2.8 Self-reactive substances and mixtures
2.9 Pyrophoric liquids
2.10 Pyrophoric solids
2.11 Self-heating substances and mixtures
2.12 Substances and mixtures which, in contact with water, emit flammable gases
2.13 Oxidising liquids
2.14 Oxidising solids
2.15 Organic peroxides
2.16 Corrosive to metals
2.17 Desensitized explosives
Notes: The physical hazard classes consider effects such as
Explosivity
Flammability
Oxidizing potential
Metal corrosion
Chemicals under pressure
The criteria for physical hazard classification are aligned with the UN recommendations on the Transport of Dangerous Goods where they are found in the Manual of Tests and Criteria, the UN Test Manual for short, also referred to as the “Orange Book”.

## Slide 6
Acute toxicity | Chronic toxicity
Single exposure | Repeated exposure
High dose | Low dose
Clinical symptoms | No overt clinical symptoms
Treatment | Treatment not always possible
Recovery | Sustained/irreversible damage
Health hazard – Toxicity in human
Notes: When the GHS refers to a health hazard it means ability to cause harm (toxicity) in humans. Thus, a health hazard in the present context is a chemical that can adversely affect human health. A distinction can be made between acute and chronic health effects. Acute toxicity is generally characterised by a single or short-term exposure at a high dose causing clinical symptoms which hopefully can be treated so the affected person recovers. One example illustrated here is mushroom poisoning. Chronic effects are more insidious as they may show after long-term and low-dose exposure that do not cause any obvious immediate effects. However, over time symptoms may develop and by the time they are recognised treatment may not always be possible. One example is lung cancer due to long-term smoking.

## Slide 7
3.1 Acute toxicity
3.2 Skin corrosion/irritation
3.3 Serious eye damage/eye irritation
3.4 Respiratory or skin sensitization
3.5 Germ cell mutagenicity
3.6 Carcinogenicity
3.7 Reproductive toxicity
3.8 Specific target organ toxicity (STOT) — single exposure
3.9 Specific target organ toxicity (STOT) — repeated exposure
3.10 Aspiration hazard
Health hazards
Notes: The GHS contains classification criteria for ten health hazard classes.
Acute toxicity refers to serious adverse health effects (i.e. lethality) occurring after a single or short-term exposure to a substance or mixture by ingestion (oral exposure), skin contact (dermal exposure) or inhalation.
Skin corrosion refers to the production of irreversible damage to the skin; namely, visible necrosis through the epidermis and into the dermis occurring after exposure to a substance or mixture, while skin irritation refers to the production of reversible damage to the skin occurring after exposure to a substance or mixture.
Serious eye damage refers to the production of tissue damage in the eye, or serious physical decay of vision, which is not fully reversible, occurring after exposure of the eye to a substance or mixture. Eye irritation refers to the production of changes in the eye, which are fully reversible, occurring after the exposure of the eye to a substance or mixture.
Respiratory sensitization refers to hypersensitivity of the airways occurring after inhalation of a substance or a mixture. Skin sensitization refers to an allergic response occurring after skin contact with a substance or a mixture.
Germ cell mutagenicity refers to heritable gene mutations, including heritable structural and numerical chromosome aberrations in germ cells occurring after exposure to a substance or mixture.
Carcinogenicity refers to the induction of cancer or an increase in the incidence of cancer occurring after exposure to a substance or mixture. Substances and mixtures which have induced benign and malignant tumours in well performed experimental studies on animals are considered also to be presumed or suspected human carcinogens unless there is strong evidence that the mechanism of tumour formation is not relevant for humans.
Reproductive toxicity refers to adverse effects on sexual function and fertility in adult males and females, as well as developmental toxicity in the offspring, occurring after exposure to a substance or mixture. Effects on or via lactation are allocated to a separate single category. Substances which are absorbed by women and have been shown to interfere with lactation, or which may be present (including metabolites) in breast milk in amounts sufficient to cause concern for the health of a breastfed child, should be classified to indicate this property hazardous to breastfed babies.
Specific target organ toxicity (STOT) – single exposure refers to specific, non-lethal toxic effects on target organs occurring after a single exposure to a substance or mixture. All significant health effects that can impair function, both reversible and irreversible, immediate and/or delayed, and not specifically addressed in GHS chapters 3.1 to 3.7 and 3.10, are included.
Specific target organ toxicity (STOT) – Repeated exposure refers to specific toxic effects on target organs occurring after repeated exposure to a substance or mixture. All significant health effects that can impair function, both reversible and irreversible, immediate and/or delayed, and not specifically addressed in GHS chapters 3.1 to 3.7 and 3.10, are included.
Aspiration means the entry of a liquid or solid chemical directly through the oral or nasal cavity, or indirectly from vomiting, into the trachea and lower respiratory system. Aspiration hazard refers to severe acute effects such as chemical pneumonia, pulmonary injury or death occurring after aspiration of a substance or mixture.

## Slide 8
4.1 Hazardous to the aquatic environment
4.2 Hazardous to the ozone layer
Chemicals covered by the Montreal protocol
Environmental hazards
Covers effects observed after both acute (short-term) and chronic (long-term) exposure.
The persistency (degradation rate) of a chemical in the environment and its bioaccumulating potential are important to consider in long-term hazard classification.
Notes: Hazardous to the aquatic environment means the intrinsic property of a substance or mixture to cause harm to an organism upon aquatic exposure. The hazard class covers both acute (short-term) and chronic (long-term) exposure. The duration of long-term exposure is determined by the life-cycle of the test organism. Important factors to consider when classifying chemicals for long-term aquatic toxicity are degradation rate and bioaccumulating potential.
Degradation means the decomposition of organic molecules to smaller molecules and eventually to carbon dioxide, water and salts.
Bioaccumulation means net result of uptake, transformation and elimination of a substance in an organism due to all routes of exposure (i.e. air, water, sediment/soil and food).
Hazardous to the ozone layer covers the controlled substances listed in Annexes to the Montreal Protocol and mixtures containing at least one of these substances as ingredient(s) at a concentration ≥ 0.1%.

## Slide 9
2
  Hazard categories

## Slide 10
Low
High
1 | 2 | 3 | 4 | 5
Each hazard class is divided into hazard categories that differentiate the hazard according to:
the severity of the effect or
weight of the evidence. (e.g. data on effects in exposed human populations carry a higher weight than experimental animal studies, thus positive data from human populations motivates classification in a higher hazard category than when solely animal data is available)
Note: Lack of observations in exposed human populations do not negate positive animal test data.
Chemicals with the most severe effect within a hazard class are generally placed in Category 1 and then the number increases with decreasing severity. The differentiating for some physical hazards looks slightly different.
Hazard categories
Notes: Each hazard class is divided into hazard categories that differentiate the hazard according to
the severity of the effect or
weight of the evidence.
Data on effects in exposed human populations carry a higher weight than experimental animal studies, thus positive data from human populations motivates classification in a higher health hazard category than when solely animal data is available.
It is important to note that lack of observations in exposed human populations do not negate positive animal test data.
Chemicals with the most severe effect within a hazard class are generally placed in Category 1 and then the number increases with decreasing severity. Some physical hazard classes are differentiated according to severity using an alternative to the numbering system.

## Slide 11
Hazard class | Hazard category |  |  |  |  |  |  |  |  |  |  |  |  |  | 
2.1 Explosives | 1 |  | 2 |  |  |  |  |  |  |  |  |  |  |  | 
 |  |  | 2A |  |  |  |  | 2B |  |  |  |  | 2C |  | 
2.2 Flammable gases | 1A |  |  |  |  |  |  |  | 1B |  |  |  |  | 2 | 
 | Flammable |  | Pyrophoric |  |  | Chemically unstable |  |  | Flammable |  |  |  |  | Flammable | 
 |  |  |  |  |  | A |  | B |  |  |  |  |  |  | 
2.3 Aerosols and chemicals under pressure | 1 |  |  | 2 |  |  |  |  |  |  | 3 |  |  |  | 
2.4 Oxidising gases | 1 |  |  |  |  |  |  |  |  |  |  |  |  |  | 
2.5 Gases under pressure | Compressed |  | Liquified |  |  |  |  | Refrigerated liquefied |  |  |  |  | Dissolved | Dissolved | 
2.6 Flammable liquids | 1 |  | 2 |  |  |  |  | 3 |  |  |  |  | 4 | 4 | 
2.7 Flammable solids | 1 |  |  |  |  |  |  | 2 |  |  |  |  |  |  | 
2.8 Self-reactive substances and mixtures | Type A | Type B |  |  | Type C |  | Type D |  |  | Type E |  | Type F |  |  | Type G
Decrease in severity
The differentiation is aligned with the UN Recommendations on the Transport of Dangerous Goods
Physical hazard classes and categories
GHS 9th revised edition (publ.2021)
Notes: This and the next slides is an attempt to summarize the physical hazard classes and their categories.
The hazard class explosives comprises explosive substances, mixtures and articles.
An explosive substance (or mixture) is a solid or liquid substance (or mixture of substances) which in itself is capable by chemical reaction of producing gas at such a temperature and pressure and at such a speed as to cause damage to the surroundings. An explosive article is an article containing one or more explosive substances or mixtures.
The hazard class flammable gases comprises flammable, pyrophoric and chemically unstable gases.
A flammable gas is a gas having a flammable range with air at 20 °C and a standard pressure of 101.3 kPa. A pyrophoric gas is a flammable gas that is liable to ignite spontaneously in air at a temperature of 54°C or below. A chemically unstable gas is a flammable gas able to react explosively even in the absence of air or oxygen.
Aerosols covers aerosol dispensers which are any non-refillable receptacles made of metal, glass or plastics and containing a gas compressed, liquefied or dissolved under pressure, with or without a liquid, paste or powder, and fitted with a release device allowing the contents to be ejected as solid or liquid particles in suspension in a gas, as a foam, paste or powder or in a liquid state or in a gaseous state.
Chemicals under pressure are liquids or solids (e.g., pastes or powders), pressurized with a gas at a pressure of 200 kPa (gauge) or more at 20°C in pressure receptacles other than aerosol dispensers and which are not classified as gases under pressure.
An oxidizing gas is any gas which may, generally by providing oxygen, cause or contribute to the combustion of other material more than air does.
Gases under pressure are gases which are contained in a receptacle at a pressure of 200 kPa (gauge) or more at 20°C, or which are liquefied or liquefied and refrigerated. The hazard class comprises compressed gases, liquefied gases, dissolved gases and refrigerated liquefied gases.
A flammable liquid means a liquid having a flash point of not more than 93°C.
A flammable solid is a solid which is readily combustible or may cause or contribute to fire through friction. Readily combustible solids are powdered, granular, or pasty substances which are dangerous if they can be easily ignited by brief contact with an ignition source, such as a burning match, and if the flame spreads rapidly.
Self-reactive substances or mixtures are thermally unstable liquid or solid substances or mixtures liable to undergo a strongly exothermic decomposition even without participation of oxygen (air). This definition excludes substances and mixtures classified under the GHS as explosives, organic peroxides or as oxidizing. A self-reactive substance or mixture is regarded as possessing explosive properties when in laboratory testing the formulation is liable to detonate, to deflagrate rapidly or to show a violent effect when heated under confinement.

## Slide 12
Hazard class | Hazard category |  |  |  |  |  |  |  |  |  |  | 
2.9 Pyrophoric liquids | 1 |  |  |  |  |  |  |  |  |  |  | 
2.10 Pyrophoric solids | 1 |  |  |  |  |  |  |  |  |  |  | 
2.11 Self-heating substances and mixtures | 1 |  |  |  |  |  | 2 |  |  |  |  | 
2.12 Substances and mixtures which, in contact with water, emit flammable gases | 1 |  |  |  | 2 |  |  |  | 3 |  |  | 
2.13 Oxidising liquids | 1 |  |  |  | 2 |  |  |  | 3 |  |  | 
2.14 Oxidising solids | 1 |  |  |  | 2 |  |  |  | 3 |  |  | 
2.15 Organic peroxides | Type A | Type B |  | Type C |  | Type D |  | Type E |  | Type F |  | Type G
2.16 Corrosive to Metals | 1 |  |  |  |  |  |  |  |  |  |  | 
2.17 Desensitized Explosives | 1 |  | 2 | 2 |  |  | 3 |  |  |  | 4 | 
Physical hazard classes and categories (cont.)
GHS 9th revised edition (publ.2021)
Decrease in severity
Notes: Pyrophoric liquid and pyrohoric solids are liquids and solids, respectively, which, even in small quantities, are liable to ignite within five minutes after contact with air.
A self-heating substance or mixture is a solid or liquid substance or mixture, which, by reaction with air and without energy supply, is liable to self-heat. The substance or mixture differs from a pyrophoric liquid or solid in that it will ignite only when in large amounts (kilograms) and after long periods of time (hours or days).
Substances or mixtures which, in contact with water, emit flammable gases are solid or liquid substances or mixtures which, by interaction with water, are liable to become spontaneously flammable or to give off flammable gases in dangerous quantities.
Oxidizing liquids and oxidizing solids are liquids and solids, respectively, which, while not necessarily combustible, may, generally by yielding oxygen, cause, or contribute to, the combustion of other material.
Organic peroxides, liquid or solid, may be considered derivatives of hydrogen peroxide, where one or both of the hydrogen atoms have been replaced by organic radicals. Organic peroxides are thermally unstable substances or mixtures, which may undergo exothermic self-accelerating decomposition. They may also be liable to explosive decomposition, burn rapidly, be sensitive to impact or friction and/or react dangerously with other substances.
A substance or a mixture which is corrosive to metals will materially damage, or even destroy, metals.
Desensitized explosives are solid or liquid explosive substances or mixtures which are treated (wetted, dissolved or diluted) to suppress their explosive properties in such a manner that they do not mass explode and do not burn too rapidly and therefore may be exempted from the hazard class “Explosives”.

## Slide 13
Hazard class | Hazard category |  |  |  | 
3.1 Acute toxicity Oral Dermal Inhalation |  |  |  |  | 
 | 1 | 2 | 3 | 4 | 5
 | 1 | 2 | 3 | 4 | 5
 | 1 | 2 | 3 | 4 | 5
3.2 Skin corrosion/irritation | Corrosive |  |  | Irritant | 
 | 1A | 1B | 1C | 2 | 3
3.3 Serious eye damage | Corrosive |  |  | Irritant | 
Skin corrosion/irritation | 1 |  |  | 2A | 2B
3.4 Sensitization Respiratory Skin |  |  |  |  | 
 | 1A |  |  | 1B | 
 | 1A |  |  | 1B | 
Health hazard classes and categories
GHS 9th revised edition (publ.2021)
Decrease in severity
Notes: The health hazard class Acute toxicity has five hazard categories. The hazard class distinguishes between route of exposure (oral, dermal and inhalation).
Skin corrosion/irritation and Serious eye damage distinguish between irreversible (corrosion) and reversible (irritation) to the skin or eye.
Sensitization makes a distinction between effects on the respiratory tract (e.g. asthma) and skin (e.g. rashes, nettle fever). Respiratory sensitization classification is based on human evidence.

## Slide 14
Hazard class | Hazard category |  |  |  | 
3.5 Germ cell mutagenicity | 1A | 1B |  | 2 | 
3.6 Carcinogenicity | 1A | 1B |  | 2 | 
3.7 Reproductive toxicity | 1A | 1B |  | 2 | Lactation
3.8 STOT – single exposure | 1 | 2 |  | 3 | 
3.9 STOT – repeated exposure | 1 |  | 2 |  | 
3.10 Aspiration toxicity | 1 |  | 2 |  | 
GHS 9th revised edition (publ.2021)
Health hazard classes and categories (cont.)
Decrease in severity
Notes: Mutagenicity, carcinogenicity and reproductive toxicity are often referred to as CMR properties and chemicals with any of these properties are often subject to strict regulation by various jurisdictions, especially when they are classified in categories 1A or 1B. Effects on or via lactation is a special hazard category within the reproductive toxicity hazard class.
One example of a chemical that causes specific target organ toxicity is methanol where human evidence shows that it can specifically damage the eye and cause blindness, even after single exposure.
Aspiration toxicity is a serious and potentially fatal effect where no test system is available. The classification criteria are based on human evidence or physico-chemical properties.

## Slide 15
Hazard class | Hazard category |  |  |  |  | 
4.1 Hazardous to the aquatic environment Acute Long-term |  |  |  |  |  | 
 | 1 |  | 2 |  | 3 | 
 | 1 | 2 |  | 3 |  | 4
4.2 Hazardous to the ozone layer | 1 |  |  |  |  | 
GHS 9th revised edition (publ.2021)
Environmental hazard classes and categories
a
Decrease in severity
Notes: Classification in the hazard class Hazardous to the aquatic environment is based on toxicity testing in aquatic organisms, such as fish, crustacea and aquatic plants. Classification is based on effects observed in the most sensitive test species.
The hazard class Hazardous to the ozone layer contains only on category.

## Slide 16
3
  Classification
  of substances

## Slide 17
Data* generated in accordance with test methods (e.g. Test guidelines adopted by the Organisation for Economic Co-operation and Development (OECD), UN Manual for Transport of Dangerous Goods);
Epidemiological data and experience** on the effects on humans, such as occupational data and data from accident databases;
Other information (to fill data gaps) including Read across, Grouping of chemicals and Quantitative Structure Activity Relationship (QSAR)
Classification of substances
*Test data is required to assess physical hazard
**Testing on humans solely for hazard identification purposes is generally not acceptable
Notes: Substances are classified based on available data obtained by internationally validated and accepted test methods. Test data is required for physical hazard classification. Classification of chemicals for effects on humans can also be based on epidemiological data or human experience. However, human testing for the purpose of classification is not acceptable. Other information, such as molecular structural information, may assist in classification.

## Slide 18
https://www.oecd-ilibrary.org/environment/oecd-guidelines-for-the-testing-of-chemicals_72d77764-en
Data based on testing in accordance with OECD test guidelines are available for a substantial number of substances.
OECD Guidelines for Testing of Chemicals
Section 1 Physical-Chemical properties
Section 2 Effects on Biotic Systems
Section 3 Environmental fate and behaviour
Section 4 Health effects
Section 5 Other Test Guidelines
Notes: The OECD Guidelines for Testing of Chemicals are accepted internationally as standard methods for safety testing. They are used by professionals in industry, academia and government involved in the testing and assessment of chemicals (industrial chemicals, pesticides, food additives, etc.). The Guidelines are elaborated with the assistance of experts from regulatory agencies, academia, industry, environmental and animal welfare organisations.
Under the OECD Mutual Acceptance of Data (MAD) system, laboratory test results that are generated in accordance with OECD Test Guidelines and OECD Principles of Good Laboratory Practices are accepted in all OECD countries and adherent countries for the purpose of safety assessment of chemicals.

## Slide 19
4
  Classification
  of mixtures

## Slide 20
Identity of ingredient substances
Hazard classification of ingredient substances
Concentration of ingredient substances
For mixtures, the classification generally requires knowledge on the identity of the ingredient substances, their individual classification, and their concentration in the mixture.
Mixtures
Classification of the mixture for a specific hazard can be based on testing (mandatory for physical hazards), by summation of the concentration of the classified ingredients or by using cut-off values/concentration limits.
Notes: The classification of mixtures generally requires knowledge of the ingredient substances, their concentration, and individual classification.

## Slide 21
Classification of mixtures for physical hazards is based on testing
Combining a flammable substance with an oxidising substance may form an explosive mixture
Physical hazard classification of mixtures
Notes: Classification of mixtures for physical hazards requires testing of the mixtures. A mixture of two substances with two different hazardous properties may result in a mixture with a third hazardous property. For example, combining a flammable substance with an oxidising substance will form an explosive mixture.

## Slide 22
Hazard class | Mixture classification method
Acute toxity | Calculation
Skin corrosion/irritation | Cut-off value/concentration limit, additive
Serious eye damage/eye irritation | Cut-off value/concentration limit, additive
Respiratory or skin sensitization | Cut-off value/concentration limit, non-additive
Germ cell mutagenicity | Cut-off value/concentration limit, non-additive
Carcinogenicity | Cut-off value/concentration limit, non-additive
Reproductive toxicity | Cut-off value/concentration limit, non-additive
STOT – single exposure | Cut-off value/concentration limit, non-additive
STOT – repeated exposure | Cut-off value/concentration limit, non-additive
Aspiration toxicity | Cut-off value/concentration limit, additive
Health hazard classification of mixtures is generally based on the available information for the individual classified ingredients and their concentrations in the mixture. Classification is derived using either a calculation method or by applying cut-off values/concentration limits methods (additive* or non-additive**).
Health hazard classification of mixtures
*E.g. Sum of classified ingredients ≥1%
**E.g. One classified ingredient present at ≥0.1%
Notes: The health hazard classification of mixtures is generally based on data on the ingredient substances. For acute toxicity, a calculation method is applied on numerical indices of acute toxicity (acute toxicity estimate, ATE) for each classified ingredient and their percentage in the mixture. For other hazard classes, a cut-off value/concentration limit approach is applied. The approach can be either additive considering the sum of concentration of all ingredients classified for a certain hazard, or non-additive where a single substance above the cut-off value/concentration limit justifies classification.

## Slide 23
Hazard class | Mixture classification method
Hazardous to the aquatic environment | Summation of the concentrations of the classified ingredients
Hazardous to the ozone layer | Cut-off value/concentration limit (at least one classified ingredient listed in the Annexes to the Montreal Protocol present in the mixture at a concentration ≥0.1%)
Environmental hazard classification of mixtures is generally based on the available information for the individual classified ingredients and their concentrations in the mixture.
Environmental hazard classification of mixtures
Notes: For environmental hazards, a summation method is applied in the case of mixtures containing substances classified as hazardous to the aquatic environment.
The cut-off value/concentration limit approach is used for mixtures containing substances classified as hazardous to the ozone layer.

## Slide 24
For more information, please contact UNITAR Globally Harmonized System of Classification and Labelling of Chemicals | UNITAR or visit the GHS website https://unece.org/about-ghs
Notes: For more information on the GHS, you can either contact UNITAR or visit the UN GHS website.