## Slide 1
Hazard communication
Notes: When hazardous properties of chemical substances and mixtures have been identified and classified based on type and severity of effects, it is important that this knowledge is passed on to the handlers and users.

## Slide 2
1
Communicating hazard information
What constitutes a GHS label?
Examples of summary tables in GHS Annex 3
Some labelling examples presented in GHS Annex 7
GHS and FAO/WHO labelling of pesticides
What is a Safety Data Sheet (SDS)?
The content of the SDS
Topics
2
3
4
5
6
7
Notes: The GHS includes provisions for hazard communication through label information and safety data sheets. In this presentation you will be able to learn more on these ways of hazard communication. It will highlight the labelling elements and the content of the safety data sheet (SDS). It also provides examples of hazard information summary tables and examples of arrangement of labelling elements found in the GHS. The content of the SDS is illustrated by examples taken from SDSs available online.

## Slide 3
  Communicating hazard information
1

## Slide 4
Right to know –
right to comprehend
How do you make users aware of the hazard?
Notes: Once a hazard has been identified the basic question is: How do you make users aware of the hazard? It is important to ensure that the information provided is not only received but also understood. Users have a right to know but they also have a right to comprehend. You should bear in mind that anything that can be misunderstood will be misunderstood, so clarity of the message and training of users is of the essence.

## Slide 5
Labelling
  Chapter 1.4
  Annex 1
  Annex 3
  Annex 5
  Annex 7
Safety Data Sheets (SDS)
  Chapter 1.5
  Annex 4
Annex 6 - Comprehensibility testing
(Annex 11 – Other hazards not resulting in classification)
Note: Annex 2 found in GHS Rev.4 has been removed in later revisions
Hazard Communication in GHS
Notes: Hazard information is addressed in several sections of the GHS. Chapter 1.4 contains details on labelling while provisions for SDS are found in Chapter 1.5.
While labelling is the only hazard information a consumer gets, professional users that handle chemicals on a daily basis, and sometimes in large quantities, requires more detailed hazard information which can be found in the SDS.
The annexes listed in connection with labelling and SDS may be helpful as they contain summary tables and examples showing for instance how classification and labelling are connected and how the communication elements can be arranged on a label.
Annex 6 presents a methodology that can be used for comprehensibility testing of information provided by labels and SDS.
Annex 11 presently addresses the formation of explosive dust under certain circumstances, a physical hazard that needs to be communicated but it is not a hazard that is classified within the GHS.

## Slide 6
2
What constitutes a GHS label?

## Slide 7
Pictograms
Signal words
Hazard statements
Precautionary statements
Additional information on label
Product identifier
Supplier identifier
Supplemental information
GHS hazard communication elements
Labelling
Notes: A label is defined as an appropriate group of written, printed or graphic information elements concerning a hazardous product, selected as relevant to the target sector(s), that is affixed to, printed on, or attached to the immediate container of a hazardous product, or to the outside packaging of a hazardous product.
The GHS hazard communication elements are:
Pictograms
Signal words
Hazard statements
Precautionary statements

## Slide 8
Flammable
Oxidiser
Corrosive
Explosive
Toxic
Serious health hazard
Hazardous to the
environment
GHS pictograms
Gas under pressure
Harmful
Notes: A GHS pictogram consists of a black symbol in a white square, set at a top and with a red frame. There are nine GSH pictograms. The black symbol indicates the hazard. The precise nature and severity of the hazard may not be intuitively clear from the symbol alone. It is therefore important to consider the symbol as an alert signal that draws the attention to other information on the label.

## Slide 9
Danger – severe hazard
Warning – less severe hazard
Signal words
Notes: The signal word is a simple signal to indicate the severity of the hazard. ”Danger” signals a more severe hazard than ”warning”.

## Slide 10
H2xx – Physical hazard
  e.g. H240 – Heating may cause an explosion
H3xx – Health hazard
  e.g. H331 – Toxic if inhaled
H4xx – Environmental hazards
  e.g. H410 – Very toxic to aquatic life with long lasting effects
Combination hazard statements possible, for instance
Fatal if swallowed, in contact with skin or if inhaled (H300, H310, H330)
Hazard statements
Notes: The hazard statement is a short phrase that explains the nature and severity of the hazard. There are hazards statements for physical hazards, health hazards and environmental hazards. The hazard statements have been codified for easy reference in summary tables or various lists. The codes should not be used on the labels as they are meaningless to most users. The codes for physical hazards start with H2 and then a two-digit number. H stands for hazard and 2 refers to the part in the GHS where classification criteria for physical hazards are found. Similarly, health hazard codes start with H3 and environmental hazards with H4. Here you can see examples of different hazard statements for the different types of hazards. It is also possible to combine hazard statements as is illustrated on the slide. The codification of hazard statements is elaborated in the GHS Annex 3 which also contains summary tables of the hazard statements.

## Slide 11
Classification |  |  | Labelling |  | 
Hazard class | Hazard category |  | Pictogram | Signal word | Hazard statement
Acute toxicity | 1 | Oral |  | Danger | Fatal if swallowed
 |  | Dermal |  |  | Fatal in contact with skin
 |  | Inhalation |  |  | Fatal if inhaled
 | 2 | Oral |  | Danger | Fatal if swallowed
 |  | Dermal |  |  | Fatal in contact with skin
 |  | Inhalation |  |  | Fatal if inhaled
 | 3 | Oral |  | Danger | Toxic if swallowed
 |  | Dermal |  |  | Toxic in contact with skin
 |  |  |  |  | Toxic if inhaled
 |  | Inhalation |  |  | 
 | 4 | Oral |  | Warning | Harmful if swallowed
 |  | Dermal |  |  | Harmful in contact with skin
 |  |  |  |  | Harmful if inhaled
 |  | Inhalation |  |  | Harmful if inhaled
 | 5 | Oral | No pictogram | Warning | May be harmful if swallowed
 |  | Dermal |  |  | May be harmful in contact with skin
 |  | Inhalation |  |  | May be harmful if inhaled
Higher
Lower
Severity
Hazard information Example 1:
Acute toxicity
Notes: This and the following slide are based on entries in the summary tables in Annex 1 of the GHS. Here you can see how hazard information related to the five categories in the hazard class Acute toxicity are communicated by pictograms, signal words and hazard statements. The hazard statements codes are not included here but you find them in the table in the GHS Annex 1. Please note how the information changes when the severity of the effect decreases. The skull and crossbones symbol are used for the top three categories, the exclamation mark for Category 4 while no pictogram is used for Category 5. You can also note that the hazard statements change from ”fatal” to ”toxic”, ”harmful” and finally ”may be harmful”.

## Slide 12
Classification |  |  |  | Labelling |  | 
Hazard class | Hazard category |  |  | Pictogram | Signal word | Hazard statement
Flammable gases | 1A | Flammable gas |  |  | Danger | Extremely flammable gas
 |  | Pyrophoric gas |  |  | Danger | Extremely flammable gas
 |  |  |  |  |  | May ignite spontaneously if exposed to air
 |  | Chemically unstable gas | A |  | Danger | Extremely flammable gas
 |  |  |  |  |  | May react explosively even in the absence of air
 |  |  | B |  | Danger | Extremely flammable gas
 |  |  |  |  |  | May react explosively even in the absence of air at elevated pressure and/or temperature
 | 1B |  |  |  | Danger | Flammable gas
 | 2 |  |  | No pictogram | Warning | Flammable gas
Hazard information Example 2:
Flammable gases
Notes: This is a summary table for the hazard categories and labelling elements within the hazard class Flammable gases. There are three primary hazard categories, 1A, 1B and 2. Category 1A differentiates between flammable gas, pyrophoric gas and chemically unstable gas. The category chemically unstable gas is divided into the subcategories A and B. Category 2 substances and mixtures do not carry a pictogram while the other categories and subcategories use the flammability pictogram and the signal word Danger. The Hazard statements used explain the severity of the hazard. You can note that category 1A has the hazard statement ”Extremely flammable gas” and in most cases a second hazard statement that explains the further differentiation. Both Category 1B and 2 use the hazard statement ”Flammable gas”.

## Slide 13
P1xx – General precautionary statements
  e.g. P102 - Keep out of reach of children
P2xx – Prevention precautionary statements
  e.g. P260 – Do not breathe dust/fume/gas/mist/vapour/spray
P3xx – Response precautionary statements
  e.g.P316 – Get emergency medical help immediately
P4xx – Storage precautionary statements
  e.g. P405 – Store locked up
P5xx – Disposal precautionary statements
  e.g. P501 - Dispose of contents/container to…
Combination precautionary statements possible, for instance
IF ON SKIN: Wash with plenty of water/…
Precautionary statements
Notes: The precautionary statements gives guidance on use and handling as well as emergency response in case of accidents. There are five different types of precautionary statements, and they are also codified with a letter, P, and a three-digit number.
The P1 series contains the general precautionary statements and the example given here is “Keep out of reach of children”.
The P2 series contains precautionary statements relating to accident prevention, such as “Do not breathe dust/fume/gas/mist/ vapour/spray.” The slash (“/”) means that the classifier has the option to choose the alternative that is most appropriate.
The P3 series gives guidance on what to do in case of exposure, such as “Get emergency medical help immediately”.
The P4 series gives guidance on how to store the labelled substance or mixture, one example is “Store locked up”.
The P5 series gives guidance on disposal and here the hazard statement “Dispose of contents/container to…” gives an option for the classifier to refer to e.g. legal obligations for hazardous waste collection and disposal.
The precautionary statements can be combined, and in some cases, they need to be combined. For instance, IF ON SKIN is a precautionary hazard statement that needs further specification, in this case by using the precautionary statement “Wash with plenty of water/…” If water is not appropriate, a more suitable washing agent should be specified instead.
The codification of precautionary statements is elaborated in the GHS Annex 3 which also contains summary tables of the precautionary statements.

## Slide 14
3
Examples of summary tables in the GHS Annex 3

## Slide 15
Matrix of precautionary statements by hazard class/category
(one example from GHS Annex 3, section 3)
Notes: The GHS Annex 3 contains matrices where the label elements for all hazard classes and each hazard category can be found. This is one example for Hazard category 1 within the hazard class Eye damage/irritation. The matrix shows the symbol for corrosion, the signal word (“Danger”) and the Hazard statement (“Causes serious eye damage”) with its code (H318). You also find the precautionary statements, in this case for prevention and response.

## Slide 16
Matrix of precautionary statements by hazard class/category
(another example from GHS Annex 3, section 3)
Notes: This example shows the label elements for hazard category 1 within the hazard class Specific target organ toxicity, single exposure. The symbol is the serious health hazard symbol, the signal word is Danger and there are options to further specify the affected target organ(s) in the hazard statement as indicated. For instance, the available data may show that the substance causes damage to eyes upon ingestion in which case this should be indicated in the hazard statement.
The precautionary statements to use for this hazard category covers prevention, response, storage and disposal. Please note that the precautionary statements contain options for specification.

## Slide 17
4
Some labelling examples presented in GHS

## Slide 18
Notes: The GHS Annex 7 provides examples on how the labelling elements can be arranged. You can see that in addition to pictograms, signal words, hazard statements and precautionary statements, in the middle panel, the label should also give the product name and contact details of the supplier. This label example also contains information on transport according to the UN system for the transport of dangerous goods.

## Slide 19
Labelling of small packaging
Notes: This is another example from Annex 7 where a kit containing multiple small containers is labelled. The outer packaging can provide more information on the content and hazards of the individual containers while these can give minimum information such as supplier, product identity, pictogram(s), signal word and a reference to the enclosed full label information.

## Slide 20
Fold-out multilingual label
Notes: Fold-out labels can be used to provide multi-lingual information. In such a case it is important that vital hazard information is completely fixed to the immediate container in case the fold-out label is torn off.

## Slide 21
5
GHS and FAO/WHO labelling of pesticides

## Slide 22
The FAO/WHO guidance recommends that the GHS should be the only classification scheme used for labelling health hazards of pesticides.
Hazard colour bands could be added to pesticide labels to take into account both acute and severe chronic health hazards, using the GHS criteria for carcinogenicity, mutagenicity and reproductive toxicity.
https://www.who.int/publications/i/item/9789240053014
FAO/WHO Guidance on Good Labelling Practice for Pesticides
Notes: The FAO/Guidance on Good Labelling Practice for Pesticides recommends that hazard classification according to the GHS should be used for labelling pesticides. The revised guidance was published in 2022 and now considers both acute and chronic health hazards.

## Slide 23
Labelling of pesticides and colour banding
Notes: In addition to the GHS label elements, the FAO/WHO Guidance includes colour banding as a means to further communicate the hazard. Red is used for the most severe hazards, then yellow and finally blue. Grey is used for products not classified. In this slide you see label guidance for products classified for acute toxicity in the left table. Severe chronic toxicity includes the GHS hazard classes carcinogenicity, germ cell mutagenicity and reproductive toxicity and the label guidance is shown in the right table.

## Slide 24
6
What is a safety data sheet (SDS) ?

## Slide 25
To provide comprehensive information about a substance or mixture for use in workplace chemical control regulatory frameworks.
To be a source of information about hazards
To provide advice on safety precautions
To act as a reference source for the management of hazardous chemicals in the workplace
Enables the employer
  to develop an active programme of worker protection measures, including training, which is specific to the individual workplace
  to consider any measures which may be necessary to protect the environment.
The role of the Safety Data Sheet (SDS)
Notes: The SDS serves to provide comprehensive information about a chemical for use at the workplace and associated regulatory frameworks.
It is a source of information about hazards and provides advice on use and safety precautions.
The SDS acts as a reference source for the management of hazardous chemicals in the workplace.
It enables the employer to develop an active programme of worker protection measures as well as to consider any measures which may be necessary to protect the environment.

## Slide 26
7
The content of the SDS

## Slide 27
Identification
Hazard identification
Composition/information on ingredients
First-aid measures
Fire-fighting measures
Accidental release measures
Handling and storage
Exposure controls/personal protection
Physical and chemical properties
Stability and reactivity
Toxicological information
Ecological information
Disposal considerations
Transport information
Regulatory information
Other information
The 16 sections of the SDS
Notes: A Safety Data Sheet developed in accordance with the GHS contains 16 sections which are listed on this slide. In the following slides, these sections are presented in some detail with illustrative examples available on the internet.

## Slide 28
Substance/mixture identification
Recommended uses
Name and contact detail of supplier
Emergency contact
Section 1: Identification
Example:
Company name
Address
Contact details (phone, fax, e-mail, web-site)
Contact details to competent person responsible for the safety data sheet
e.g. National Poison
Information Centre
Notes: The first section of the SDS contains information on the chemical, recommended use and details of the supplier. The supplier details in the example have been masked.

## Slide 29
2.1 Classification of the substance or mixture
Type and severity of hazard
2.2 Label elements
Pictogram
Signal word
Hazard statement(s)
Precautionary statement(s)
2.3 Other hazards that do not result in classification
The section should include a brief and easily understood summary/conclusion of the data behind the classification
Section 2: Hazard identification
Example:
Notes: Section 2 contains information on the type and severity of the hazard as well as labelling information. This information shall of course correspond to the package label.

## Slide 30
Substance name
CAS number, IUPAC name
Mixtures:
Concentration or concentration interval of ingredient substances
Section 3: Composition/information on ingredients
Example:
Notes: Information on ingredients is found in Section 3. In this case it is a pure substance, namely acetone.

## Slide 31
Mixture
Example:
Notes: This is an example of Section 3 in a SDS of a mixture. Each ingredient should be specified along with the concentration or concentration interval in the mixture. The information is essential for chemical inspection authorities to ensure that the mixture is correctly classified and labelled in accordance with legislation, though it is also useful for formulators and other users.

## Slide 32
Section 4: First aid measures
Example:
Notes: The first-aid measures presented in Section 4 should be in line with the precautionary statements.

## Slide 33
Section 5: Fire-fighting measures
Example:
Notes: Section 5 of the SDS contains information on measures to be taken in case of fire, including suitable extinguishing media. This is essential information for firefighters and rescue services.

## Slide 34
Personal precautions, protective equipment and emergency procedures
For non-emergency personnel
For emergency responders
Environmental precautions
Methods and materials for containment and cleaning up
Section 6: Accidental release measures
Example:
Notes: In case of a spill or accidental release of the chemical covered by the SDS, actions to be taken are found in Section 6. The section considers both personal protection and how to avoid or minimize environmental impact. It also gives advice on cleaning up procedures and suitable materials.

## Slide 35
Section 7: Handling and storage
Example:
Notes: Section 7 on precautions for handling and storage should be in line with the precautionary statements.

## Slide 36
Control parameters
e.g. occupational exposure limits
Appropriate engineering controls
Individual protection measures, such as personal protective equipment (PPE)
Eye/face
Skin
Respiratory
Section 8: Exposure controls/personal protection
Example:
Notes: Section 8 gives additional information on personal protection, including technical specifications on what type of material to use to protect skin, eyes and airways. It also contains workplace control parameters such as occupational exposure limits.

## Slide 37
Physical state
Colour
Odour
Melting point/freezing point
Boiling point or initial boiling point and boiling range
Flammability
Lower and upper explosion limit/flammability limit
Flash point
Auto-ignition temperature
Decomposition temperature
pH
Kinematic viscosity
Solubility
Partition coefficient: n-octanol/water (log value)
Vapour pressure
Density and/or relative density
Relative vapour density
Particle characteristics
Section 9 was extensively revised in GHS Rev.6, Annex 4
Section 9: Physical and chemical properties and safety characteristics
Notes: Section 9 presents the physical and chemical properties of the chemical. This section of the SDS was extensively revised in GHS revision 6, published in 2015.

## Slide 38
Reactivity
Chemical stability
Possibility of hazardous reactions
Conditions to avoid (e.g. static discharge, shock or vibration)
Incompatible materials
Hazardous decomposition products
Section 10: Stability and reactivity
Notes: Section 10 also refers to physical properties of the chemical, focusing on reactivity, stability and how to ensure safe handling.

## Slide 39
Delayed and immediate health effects
Chronic health effects from short and long-term exposure
Likely routes of exposure
Symptoms
Numerical measures of toxicity (e.g. acute toxicity estimates, ATE)
Sources of information
Section 11: Toxicological information
Notes: Section 11 is used primarily by medical professionals, occupational health and safety professionals and toxicologists. A concise but complete and comprehensible description of the various health effects, and the available data used to identify those effects, should be provided.

## Slide 40
Toxicity
Persistence and degradability
Bioaccumulative potential
Mobility in soil
Other adverse effects
Section 12: Ecological information
Notes: The aim of the information provided in Section 12 is to enable evaluation of the environmental impact of the substance or mixture if it is released to the environment. This information can assist in handling spills, and evaluating waste treatment practices, control of release, accidental release measures, and transport. A concise but complete and comprehensible description of the various ecotoxicological (environment) properties, and the available data used to identify those properties, should be provided.

## Slide 41
Section 13: Disposal considerations
Example:
Notes: Section 13 provides information for proper disposal, recycling or reclamation of the chemical and/or its container to assist in the determination of safe and environmentally preferred waste management options, consistent with legal requirements. Note that safety precautions for persons conducting disposal, recycling or reclamation activities is found in section 8 (exposure controls and personal protection) of the SDS.

## Slide 42
UN number
UN proper shipping name
Transport hazard class(es)
Packing group, if applicable
Environmental hazards (e.g.: Marine pollutant (Yes/No))
Transport in bulk according to International Maritime Organisation (IMO) instruments
Special precautions which a user needs to be aware of, or needs to comply with, in connection with transport or conveyance either within or outside their premises
Section 14: Transport information
Example:
Notes: Section 14 provides basic classification information for the transport of the chemical by road, rail, sea or air.

## Slide 43
Section 15: Regulatory information
Example:
Notes: Section 15 refers to any other regulatory information on the chemical that is not provided elsewhere in the SDS. In this example, where the chemical is placed on the EU market, you see reference to EU chemical legislation. In case the chemical is covered by the chemical conventions, i.e. the Montreal protocol, the Stockholm convention or the Rotterdam convention, this information should be provided here.
Montreal Protocol means the Montreal Protocol on Substances that Deplete the Ozone Layer, as either adjusted and/or amended.
Stockholm Convention means the Stockholm Convention on Persistent Organic Pollutants.
Rotterdam Convention means the Rotterdam Convention on the Prior Informed Consent Procedure for Certain Hazardous Chemicals and Pesticides in International Trade.

## Slide 44
For example:
Date of preparation of the latest revision of the SDS, with an explanation of the changes made
Key/legend to abbreviations and acronyms used in the SDS
Key literature references and sources for data used to compile the SDS
Section 16: Other information
Notes: Finally, section 16 provides additional information relevant to the preparation of the SDS. This includes e.g. the date of preparation of the latest revision of the SDS, a key or legend to abbreviations and acronyms used, and key literature references and sources for data used to compile the SDS.

## Slide 45: For more information, please contact UNITAR Globally Harmonized System of Classification and Labelling of Chemicals | UNITAR or visit the GHS website https://unece.org/about-ghs
Notes: For more information on GHS, you can either contact UNITAR or visit the UN GHS website.